Brandon Swanson CS 325 Project 3 11/15/15
Problem 1:

A) Lindo code used to generate solution
min 10 p1w1 + 15 p1w2 +
11 p2w1 + 8 p2w2 +
13 p3w1 + 8 p3w2 + 9 p3w3 +
14 p4w2 + 8 p4w3 +

5 w1r1 + 6 w1r2 + 7 w1r3 + 10 w1r4 +
12 w2r3 + 8 w2r4 + 10 w2r5 + 14 w2r6 +
14 w3r4 + 12 w3r5 + 12 w3r6 + 6 w3r7

st
!supply constraints
p1w1 + p1w2 <=150
p2w1 + p2w2 <=450
p3w1 + p3w2 + p3w3 <=250
p4w2 + p4w3 <=150

!warehouse input = output constraint
w1r1 + w1r2 + w1r3 + w1r4 - p1w1 - p2w1 - p3w1 = 0
w2r3 + w2r4 + w2r5 + w2r6 - p1w2 - p2w2 - p3w2 - p4w2 = 0
w3r4 + w3r5 + w3r6 + w3r7 - p3w3 - p4w3 = 0

!demand constraints
w1r1 >= 100
w1r2 >= 150
w1r3 + w2r3 >= 100
w1r4 + w2r4 + w3r4 >= 200
w2r5 + w3r5 >= 200
w2r6 + w3r6 >= 150
w3r7 >= 100

!nonegativity constraint
p1w1 >0
p1w2 >0
p2w1 >0
p2w2 >0
p3w1 >0
p3w2 >0
p3w3 >0
p4w2 >0
p4w3 >0
w1r1 >0
w1r2 >0
w1r3 >0
w1r4 >0
w2r3 >0
w2r4 >0
w2r5 >0
w2r6 >0
w3r4 >0
w3r5 >0
w3r6 >0
w3r7 >0

end

Minimum Costs: $17100
Routes:
P1 to W1 :150
P2 to W1 :200 P2 to W2 :250
P3 to W2 :150 P3 to W3 :100
P4 to W3 :150
W1 to R1 :100 W1 to R2 :150 W1 to R3 :100
W2 to R4 :200 W2 to R5 :200
W3 to R6 :150 W3 to R7 :100

B) It is infeasible without warehouse 2, there is no way to meet all the demands of the retailers.
R4 is 50 units short.

Lindo code used to verify:
min 10 p1w1 + 11 p2w1 + 13 p3w1 + 9 p3w3 + 8 p4w3 +

5 w1r1 + 6 w1r2 + 7 w1r3 + 10 w1r4 +
14 w3r4 + 12 w3r5 + 12 w3r6 + 6 w3r7

st
!supply constraints
p1w1 <=150
p2w1 <=450
p3w1 + p3w3 <=250
p4w3 <=150

!warehouse input = output constraint
w1r1 + w1r2 + w1r3 + w1r4 - p1w1 - p2w1 - p3w1 = 0
w3r4 + w3r5 + w3r6 + w3r7 - p3w3 - p4w3 = 0

!demand constraints
w1r1 >= 100
w1r2 >= 150
w1r3 >= 100
w1r4 + w3r4 >= 200
w3r5 >= 200
w3r6 >= 150
w3r7 >= 100

!nonegativity constraint
p1w1 >0
p2w1 >0
p3w1 >0
p3w3 >0
p4w3 >0
w1r1 >0
w1r2 >0
w1r3 >0
w1r4 >0
w3r4 >0
w3r5 >0
w3r6 >0
w3r7 >0

end

To verify the solution I also added just this single constraint to the original problem 1 lindo file:
w2r3 + w2r4 + w2r5 + w2r6 + p1w2 + p2w2 + p3w2 + p4w2 = 0
C) It is feasible to meet all the demands with the reduced capacity of warehouse 2 with an increased cost of $18300
to get this solution the the following constraint was added
p1w2 + p2w2 + p3w2 + p4w2 = 100
It was only necessary to constrain the routes from production to warehouse because there are already constraints in place to ensure input and output of the warehouses are equal.

Minimum Cost: 18300
Routes:
P1 to W1: 150	P2 to W1: 350	P2 to W2: 100	P3 to W3: 250
P4 to W3: 150	W1 to R1: 100	W1 to R2: 150	W1 to R3: 100
W1 to R4: 150	W2 to R4: 50	W2 to R5: 50	W3 to R5: 150
W3 to R6: 150	W3 to R7: 100